Electromagnetic waves exist with an enormous range of frequencies. This continuous range of frequencies is known as the electromagnetic spectrum. The entire range of the spectrum is often broken into specific regions. The subdividing of the entire spectrum into smaller spectra is done mostly on the basis of how each region of electromagnetic waves interacts with matter. The diagram below depicts the electromagnetic spectrum and its various regions. The longer wavelength, lower frequency regions are located on the far left of the spectrum and the shorter wavelength, higher frequency regions are on the far right. Two very narrow regions within the spectrum are the visible light region and the X-ray region. You are undoubtedly familiar with some of the other regions of the electromagnetic spectrum. The focus of Lesson 2 will be upon the visible light region - the very narrow band of wavelengths located to the right of the infrared region and to the left of the ultraviolet region. Though electromagnetic waves exist in a vast range of wavelengths, our eyes are sensitive to only a very narrow band. Since this narrow band of wavelengths is the means by which humans see, we refer to it as the visible light spectrum. Normally when we use the term "light," we are referring to a type of electromagnetic wave which stimulates the retina of our eyes. In this sense, we are referring to visible light, a small spectrum of the enormous range of frequencies of electromagnetic radiation. This visible light region consists of a spectrum of wavelengths, which range from approximately 700 nanometers (abbreviated nm) to approximately 400 nm; that would be 7 x 10-7 meter to 4 x 10-7 meter. This narrow band of visible light is affectionately known as ROYGBIV. Each individual wavelength within the spectrum of visible light wavelengths is representative of a particular color. That is, when light of that particular wavelength strikes the retina of our eye, we perceive that specific color sensation. Isaac Newton showed that light shining through a prism will be separated into its different wavelengths and will thus show the various colors that visible light is comprised of. The separation of visible light into its different colors is known as dispersion. Each color is characteristic of a distinct wavelength; and different wavelengths of light waves will bend varying amounts upon passage through a prism; for these reasons, visible light is dispersed upon passage through a prism. Dispersion of visible light produces the colors red (R), orange (O), yellow (Y), green (G), blue (B), indigo (I), and violet (V). It is because of this that visible light is sometimes referred to as ROY G. BIV. The red wavelengths of light are the longer wavelengths and the violet wavelengths of light are the shorter wavelengths. Between red and violet, there is a continuous range or spectrum of wavelengths. The visible light spectrum is shown in the diagram below. When all the wavelengths of the visible light spectrum strike your eye at the same time, white is perceived. Thus, visible light is sometimes referred to as white light. Technically speaking, white is not a color at all, but rather the combination of all the colors of the visible light spectrum. If all the wavelengths of the visible light spectrum give the appearance of white, then none of the wavelengths would lead to the appearance of black. Once more, black is not actually a color. Technically speaking, black is merely the absence of the wavelengths of the visible light spectrum. So when you are in a room with no lights and everything around you appears black, it means that there are no wavelengths of visible light striking your eye as you sight at the surroundings.

### http://www.glenbrook.k12.il.us/gbssci/phys/Class/light/u12l2a.html (above information)

# Spectral Colors

In a rainbow or the separation of colors by a prism we see the continuous range of spectral colors (the visible spectrum). A spectral color is composed of a single wavelength and can be correlated with wavelength as shown in the chart below ( a general guide and not a precise statement about color). It is safe enough to say that monochromatic light like the helium-neon laser is red (632 nm) or that the 3-2 transition from the hydrogen spectrum is red ( 656 nm) because they fall in the appropriate wavelength range. But most colored objects give off a range of wavelengths and the characterization of color is much more than the statement of wavelength. Perceived colors can be mapped on a chromaticity diagram.

|  | The C.I.E. Chromaticity Diagram On the CIE chromaticity diagram at left, some annotation is made about the significance of different parts of the diagram. The boundary represents maximum saturation for the spectral colors, and the diagram forms the boundary of all perceivable hues. |
| --- | --- |

http://hyperphysics.phy-astr.gsu.edu/hbase/vision/c4